## Slide 1: Session 6
NAD1001: INTRODUCTION TO ARCHITECTURAL DESIGN

## Slide 3: Elevation View and Other Drawings
Source: Design Drawing by Francis D. K. Ching

## Slide 4: Projection System

## Slide 5: Projection System

## Slide 6: Elevation Drawing
An essential part of the design and drafting process
Elevations are orthographic drawings showing outside/exterior views of the building
Typically four(4) elevations are drafted
Information provided may include: roofing material, roof overhangs/slopes, siding or other exterior materials, chimney heights and materials, grading data, and footing depths
Source: Pinterest

## Slide 7: Information Contained in Elevation
The appearance of a building
Vertical dimensions
Building materials
Source: Pinterest

## Slide 8: Orientation
Mechanical or engineering drafting, the elevations are described as the front, side, and rear.
In architecture, exterior elevations are called North, South, East and West.
Source: Pinterest

## Slide 9: How to obtain dimensions for elevations?
You can draft exterior elevations by directly projecting sizes from the plan views or sections.

## Slide 10: How to obtain dimensions for elevations?

## Slide 11: Material Detail
Source: Design Drawing by Francis D. K. Ching

## Slide 12: Material Detail
Source: Design Drawing by Francis D. K. Ching

## Slide 13: From Conceptual to Documentation
Source: Pinterest

## Slide 14: From Conceptual to Documentation
Source: Pinterest

## Slide 15: From Conceptual to Documentation
Source: Pinterest

## Slide 16: From Conceptual to Documentation
Source: Pinterest

## Slide 17: From Conceptual to Documentation
Source: Pinterest

## Slide 18: Elevation as a Key Design Driver
Steven Holl Glassell School of Art
Source: Steven Holl Architects

## Slide 19
Activity: Match the Elevation

## Slide 20: Cross Section (Section Drawing)
Definition: A section drawing cuts through a portion of a building vertically and is used to view the interior spaces.
Purpose: To show the relationships between different levels of a building, including floor and ceiling heights.
Section drawings provide insight into the vertical dimensions of spaces, helping to understand the scale and connection between different parts of the building.
Source: ArchDaily

## Slide 21: Section Cut

## Slide 22: Section Cut
a vertical slice cut through a two‐story residence.
Source: ArchDaily

## Slide 23: Identification of sections

## Slide 24: Section and Architectural Details
To further examine the various roof, floor, and wall conditions found at the location of that particular slice, we can enlarge the elements and then call it a detail.
Source: ArchDaily

## Slide 25: Section and Architectural Details
Source: ArchDaily

## Slide 26: Information in Section Drawing
1. Type of foundation
2. Floor system
3. Exterior and interior wall construction
4. Beam and column sizes and their material
5. Plate or wall heights
6. Floor elevations
7. Floor members, size, and spacing
8. Floor sheathing, material, and size
9. Ceiling members, size, and spacing
10. Roof pitch
11. Roof sheathing, material, and size
12. Insulation requirements
13. Finished roof material
14. Ceiling heights
Source: ArchDaily

## Slide 27: Information in Section Drawing
1. Type of foundation
2. Floor system
3. Exterior and interior wall construction
4. Beam and column sizes and their material
5. Plate or wall heights
6. Floor elevations
7. Floor members, size, and spacing
8. Floor sheathing, material, and size
9. Ceiling members, size, and spacing
10. Roof pitch
11. Roof sheathing, material, and size
12. Insulation requirements
13. Finished roof material
14. Ceiling heights

## Slide 28: Other Information from Sections

## Slide 29: Section Scale V.S. Section Detail Scale
The number of sections required varies, depending on the design and structural complexity of the building.
Source: VCE Technical Drawing Speciﬁcations

## Slide 30: Section Typology
Match the type of section drawing
1. 2D section
2. Rendered section
3. Section perspective
4. Section detail (construction drawing)
Source: ArchDaily

## Slide 31: Design with Section
Section can also be a design method.
Source: Manual of Section

## Slide 32: Design with Section
Section can also be a design method.
Source: Manual of Section

## Slide 33: Design with Section
Section can also be a design method.
Source: Manual of Section

## Slide 34: Section Showcase
Intesa Sanpaolo Office Building – Renzo Piano
Source: ArchDaily

## Slide 35: Now to the technical – Ways to Produce Section Drawing
Hand Sketch
https://www.youtube.com/watch?v=98PALn5XG0U
3D Modeling or 2D Modeling then Photoshop (standard workflow)
https://www.youtube.com/watch?v=bDl91Z3v5RY
We will learn this when we use REVIT.
More discussions will come when we talk about documentation in week 3. Australian standard does address section and elevation drawings.

## Slide 36
Activity: Section Exercise

## Slide 37
Pinterest. (2025). Pinterest Image. https://www.pinterest.com/
Steven Holl Architects. (2025). Steven Holl Projects. https://www.stevenholl.com/
Ching, F. (2023). Design Drawing. Wiley
Pinterest. (2025). Pinterest Image. https://www.pinterest.com/
Arch Daily. (2025). Arch Daily Image. https://www.archdaily.com/
Lewis, P. (2016). Manual of Section. Princeton Architectural Press
Victorian Curriculum and Assessment Authority. (2018). Technical Drawing Specifications Resource: A guide to support VCE Visual Communication Design study design 2018–22. https://www.scribd.com/document/383339569/VCE-Technical-Drawing-Specs
References

## Slide 38: Thank you Questions?